## Slide 1
Water Technology
Hardness-definition, types of hardness and determination by EDTA method-numerical problems.
Determination of dissolved (DO) oxygen by Winkler’s method.
Biological Oxygen Demand (BOD)-definition, determination and numerical problems.
Chemical Oxygen Demand (COD)-definition, determination and numerical problems.

## Slide 2
Types of water
Soft water : water that gives foam with the soap
Hard water : water that gives precipitate with the soap.
Hard water must be subjected for treatment to remove hardness by either physical method or chemical method
Physical methods : Reverse osmosis, distillation, ion exchange methods
Chemical Method: NaHCO3 method

## Slide 3
Total Hardness = Temporary hardness + Permanent hardness
Hardness of water: Hardness of water is a property of water that measures of its capacity to precipitate soap. It gives the magnitude of the soluble salts present in water and responsible for making the water hard.
Types of hardness:
There are two types of hardness-
Temporary Hardness (Carbonate hardness): This type of hardness is due to dissolved bicarbonates of Ca and Mg. It can be removed by boiling.
For example:
Ca(HCO3) 2 ( in water) ( boil for 20 -30 minutes)----> CaCO3 (ppt) + H 2O + CO2.
Permanent Hardness (Non- carbonate hardness): This type of hardness is due to soluble non-carbonate salts of Ca, Mg etc, namely, chlorides, nitrates, sulphates, hydroxides etc. They cannot be removed by heating. They need special chemical treatments to remove them.
A water sample may contain both types of hardness and hence,

## Slide 4
1. Parts per million (ppm):
It is the number of parts of calcium carbonate equivalent hardness per million (106) parts of water
1 ppm = 1 part of CaCO3 equivalent hardness in 106 parts of water
3. Degree of General Hardness (dGH or German degree): It is defined as 10 mg/L CaCO3 or 17.848 ppm.
General classification of soft and hard waters: (mg/L or ppm)
a. Soft: 0 - 17.1
b. Slightly hard: 17.1 – 60
c. Moderately hard: 60 – 120
d. Hard: 120-180
e. Very hard: 180 and above.
2. Milligram per litre (Mg/L):
It is the number of milligrams of CaCO3 equivalent hardness in 1 litre of water.
Units of Hardness of water:
Hardness of water is expressed in several ways

## Slide 5
Determination of Hardness of Water (EDTA Method)
Principle: To a sample of hard water containing Ca or Mg salts, when the blue coloured Eriochrome Black-T (EBT) indicator is added at pH 10, it forms a wine-red complex with Ca or Mg ions. However, when it is titrated against a solution of EDTA, Ca and Mg ions from the Ca-EBT complex react with EDTA releasing free EBT which is blue in colour. By knowing the quantity of EDTA required it is possible to find the hardness of water
Ca2+ + EBT indicator (blue) ------> Ca-EBT complex (Wine red)
(in hard water)
Ca-EBT complex (wine red) + EDTA ----> [Ca-EDTA] + EBT
(Blue)

## Slide 6
1:1
Disodium salt of EDTA
M2+

## Slide 7
Std. EDTA
Hard water (M ions)
+ Buffer
+ EBT Indicator
M
+
EBT
M-EBT
colorless
Wine red color
M-EBT
+
EDTA
M-EDTA
Colorless
+
EBT
Blue
Colorless
Wine red color
Blue

## Slide 8
Preparation of Std EDTA solution:
Dissolve a known wt. of soluble salt of EDTA in water in a 250 ml std. flask and add 2mL of ammonia, make up to the mark with water and mix well. Let its molarity be ‘x’ M.
a. Determination of Total hardness:
Pipette out 25 ml of the water sample in to a clean conical flask. Add 2 ml of NH3- NH 4Cl buffer and a pinch of EBT indicator. Titrate this against std. EDTA solution, until the colour changes from wine red to just blue. Notedown the volume of EDTA consumed, (say V1 ml).
Procedure:
Weight of the compound x 1000
Molecular weight of the compound x Volume
Molarity =
‘X’ M =
Wt of EDTA salt x 4
Mol. Wt of EDTA salt

## Slide 9
Calculations:
1000ml of 1 M EDTA = 100 g. of CaCO 3
Total hardness =
then
V1 ml of ‘X’ M EDTA. =
V 1 x X x 100
1000 x 1
= ‘A’ g. of CaCO 3 in 25 ml water sample.
A
25
X 10 6 = D ppm of caco3

## Slide 10
b. Determination of Permanent Hardness:
Pipette out 25 ml of the same water sample in to a beaker, boil gently for 20-30 minutes, cool and filter in to a conical flask. To the filtrate add 2 ml NH 3- NH 4 Cl buffer and a pinch of EBT indicator. Titrate this against the same std. EDTA until the colour changes from wine red to just blue. Note the volume of EDTA consumed, say V2 ml.

## Slide 11
Calculations:
1000ml. of 1 M. EDTA = 100 g. of CaCO 3
∴ Permanent Hardness=
Then,V2 ml of ‘X’ M EDTA. =
V2 x X x 100
1000 x 1
= ‘B’ g. of CaCO 3 in 25 ml boiled water sample.
B
25
X 10 6 ppm
c. Calculation of Temporary Hardness:
∴, Temporary hardness = Total hardness - Permanent hardness
Total Hardness = Temporary hardness + Permanent Hardness

## Slide 12
Dissolved Oxygen Content and its determination:
Dissolution of atmospheric oxygen in water at its partial pressure is said dissolved oxygen content in water. Algae and rooted aquatic plants also give out oxygen in to water through photosynthesis.

## Slide 13
Dissolved oxygen is required to survive the aquatic animals and also used for biological oxidation of the pollutants. But, oxygen being an oxidizing agent,hence, it causes corrosion of metallic structures in industry.
Excessive O2 (Hyperoxia) : high corrosion of metal structures and oxidative stress in body by excessive O2 2- radicals produced
Low O2 (Hypoxia): high growth of unaerobic bacteria, foul smell, death of the aquatic animals

## Slide 14
DO in water is determined by Winkler’s method.
Principle:
When a strong alkaline solution of MnSO4 (divalent) is added to a water sample containing dissolved oxygen, it picks up oxygen to form basic MnO(OH)2 ( tetravalent), that gives [O] in acidic medium ,which is used to oxidize KI to I2. The liberated Iodine is found by titrating against a standard Na2S2O3 thereby oxygen content is estimated.

## Slide 15
MnSO4 + 2 KOH ---------- > Mn (OH)2 + K2 SO4
2Mn (OH )2 + O2 (Dissolved Oxygen)--- > 2 MnO (OH )2
MnO (OH )2 + H2SO4 ----- > MnSO4 + 2H2O + [O]
2 KI + H2 SO4 + [O] -------- > K2SO4 + H2O + I2
I2 + 2 Na2S2O3 -------------- > 2 NaI + Na2 S2 O4

## Slide 16
In a stoppered bottle, 300 ml of water sample is taken and add 3 ml MnSO4, 3 ml alkaline KI. Now , Stopper the bottle and shake well for 10 to 15 minutes. Allow to stand for 2 minutes. Then add 1 ml conc. H2 SO4 and mix well to dissolve MnO2 ppt and to liberate I2.
Pipette out 100 ml of the above solution in to a conical flask and titrate against standard Sodium thiosulphate solution until the blue colour is just discharged .2 ml of starch solution as indicator added near the end point. Note the volume of Na2S2O3 required (say V1 ml).
Procedure:
300 ml water sample
3 ml MnSO4
3 ml alkaline KI
I2
1 ml conc. H2 SO4
100 ml

## Slide 17
Std. Na2S2O3
I2
I2 + 2 Na2S2O3 -------------- > 2 NaI + Na2 S4 O8
Sodium
dithionite
Sodium
Iodide
Starch as
an indicator

## Slide 18
Volume of water sample taken = 100 ml
Volume of Na2S2O3 consumed = V1 ml
Normality of Na2S2O3 used = N1
Calculations:
⸪ Wt. = Normality x Equivalent wt of the compound
Volume of water sample taken = V2 ml,
Volume of Na2S2O3 = V1 ml
Normality of Na2S2O3 = N1
Normality of D.O in water = N2
N1V1 = N2V2
D. O in water
Na2S2O3
now, weight of D.O in mg = N B X Eq. wt of O2 x1000 = D1 mg O2 /dm3
N2 = (N1 X V1)/ V2

## Slide 19
BOD is only measurement of consumed oxygen by aquatic microorganisms to decompose or oxidize organic matter.
COD refers the requirement of dissolved oxygen for the oxidation of both organic and inorganic constituents
BOD
COD

## Slide 20
Dissolved oxygen cannot be directly estimated by volumetric titration since oxygen does not react with sodium thiosulfite. However, as oxygen being an oxidizing agent ,it must need to be estimated in an indirect way.i.e winkler’s method
Determination of BOD in waste water (Winkler’s Method)
Biological Oxygen Demand (B.O.D)
Sewage water contains a lot of organic pollutants which undergo anaerobic oxidation to give products with stinking smell. Such waste water requires oxygen for the oxidation.
Definition: “The amount of oxygen required in milligrams for the biological oxidation of organic matters under aerobic condition, present in one liter of waste water over an incubation period of five days at 20o C, is called biological oxygen demand”.
Oxygen present in water is capable of oxidizing the biologically oxidizable pollutants, with the help of bacteria and in this way the oxygen in water is consumed.

## Slide 21
Determination of B.O.D:
Principle: When a sample of water containing dissolved oxygen is treated with MnSO4 and alkaline KI solutions, dissolved oxygen oxidizes Mn2+ to Mn4+. On acidification Mn4+ liberates I2 from KI which is estimated by standard NasS2O3. By determining the dissolved O2 content in water before and after incubation period it is possible to find B.O.D
Procedure:
a) Preparation of Two separate diluted waste water sample: Pipette out a known volume of sewage water sample (‘A’ ml) and dilute it to a known volume (‘B’ ml) by adding dilution water containing free oxygen and nutrients. Fill in two bottles.
‘A’ ml
‘B’ ml
1
2

## Slide 22
b) Blank titration: In bottle -1 find D.O immediately as follows: Add 3 ml MnSO4 + 3 ml alkaline KI. Stopper the bottle and mix well for 10-15 minutes. Wait for 2 minutes and then add 1 ml conc. H2SO4 to dissolve MnO2 ppt and to liberate I2. A known volume of this solution (‘V’ ml) is titrated against std. Na2S2O3 using 2 ml of starch as indicator near the end point. Note the volume of Na2 S2O3 required (say V1 ml).
Std. Na2S2O3
I2
I2 + 2 Na2S2O3 -------------- > 2 NaI + Na2 S2 O4
Sodium
dithionite
Sodium
Iodide
Starch as
an indicator
1

## Slide 23
c) Back/sample titration: Bottle -2 is incubated at 20o C for 5 days . After 5 days, add 3 ml MnSO4 + 3 ml alkaline KI. Stopper the bottle and mix well for 10-15 minutes. Wait for 2 minutes and then add 1 ml of conc. H2 SO4 to dissolve MnO2 ppt and to liberate I2. Pipette out same known volume of this solution (‘V’ ml) and titrate against the same std. Na2S2O3 as above. Note the volume Na2 S2O3 required (say V2 ml).
2
Incubated
for 5 days
at 20o C
Std. Na2S2O3
I2
I2 + 2 Na2S2O3 -------------- > 2 NaI + Na2 S2 O4
Sodium
dithionite
Sodium
Iodide
Starch as
an indicator

## Slide 24
Calculations:
1) D.O from Blank titration:
Volume of water sample taken = 100 ml,
Volume of Na2S2O3 = V1 ml
Normality of Na2S2O3 = N1
Normality of D.O in water = N B
N B = (N1 X V1)/ 100
now, weight of D.O in mg = N B X Eq. wt of O2 x1000 = D1 mg O2 /dm3

## Slide 25
2) D.O from back /sample titration: [bottle-2]
Volume of water sample = 100 ml,
(After 5 days)
Volume of Na2S2O3 = V2 ml.
Normality of Na2S2O3 = N1
Normality of D.O in bottle -2= (N1 V2)/100 = NS. Normality of DO in bottle-2 after 5 days over
weight of D.O in mg = Ns X Eq. Wt of O2 x 1000 = D2. mg/dm3
Therefore, B.O.D of the sample = (D1- D2) (B/A) =…Z……mg O2 dm-3

## Slide 26
Chemical Oxygen Demand (C.O.D)
Effluent coming out of domestic and industrial areas contain both biologically oxidizable organic pollutants and chemically oxidizable organic and inorganic pollutants. For oxidation of such pollutants a strong oxidizing agent such as K2 Cr2 O7 which can release a large amount of oxygen is required.
Definition: “The amount of oxygen in milligrams used in the chemical oxidation of biologically oxidizable, organic and inorganic pollutants in presence of acidified K2 Cr2 O7,present in one liter of waste water is called chemical oxygen demand”.
COD gives the total oxidizable impurities including biologically oxidizable, and chemically oxidizable organic and inorganic matters in the sewage.

## Slide 27
Determination of C.O.D:
Principle:
A known volume of waste water sample is taken and refluxed with a known quantity of K2Cr2 O7 solution in H2SO4 in presence of Ag2 SO4 (to catalyze the oxidation of straight chain organic compounds) and Hg SO4 (to avoid the interference of chloride by forming a soluble complex). The amount of K2 Cr2O7 unconsumed is titrated and there by calculated consumed K2 Cr2O7 Which corresponds to C.O.D of the sample.
silver sulfate (Ag2 SO4 ) as a catalyst, and mercuric sulfate (HgSO4 ) added to remove interference of chlorides.
Organic and Inorganic
K2Cr2O7
Ag2 SO4
Hg SO4
K2Cr2O7
F. A. S
To know remaining K2 Cr2O7

## Slide 28
Preparation of Std. F.A.S solution: Dissolve a known weight of F.A.S in water with a few mL of dil.H2SO4 in a 250 ml Std. volumetric flask and make up to the mark with water and mix well.
Let its Normality be
Procedure:
F.A.S
dil.H2SO4
Wt. of F.A.S x 4
Equivalent wt. of F.A.S
Normality =
Weight of the compound x 1000
Molecular weight of the compound x Volume
Molarity =
250 ml

## Slide 29
b) Back Titration: A known volume of waste water sample is taken (V) ml in to a conical flask and 1 g. of Ag2 SO4 and 1 g. of Hg SO4 are added, followed by a known volume of K2Cr2O7 acidified by H2SO4. The solution is refluxed for 20-30 min. Cooled and filtered. The filtrate is titrated against a standard FAS solution using ferroin as indicator. The colour changes of this titration is from bluish green to reddish brown color .Note the volume of F.A.S required (say, Bml).
Std. F.A.S
K2Cr2O7
Ferroin
[Fe]2+
Reddish Brown
K2Cr2O7
Ferroin
[Fe]3+
Bluish Green
Organic and Inorganic
K2Cr2O7
Ag2 SO4
Hg SO4
K2Cr2O7
F. A. S
To know remaining K2 Cr2O7
End point- Bluish green to reddish brown

## Slide 30
c) Blank titration: The above procedure is repeated by taking the same volume of distilled water instead of waste water sample. Note the volume of FAS required after titration (say, C ml)
No waste water
(No Organic and Inorganic)
K2Cr2O7
Ag2 SO4
Hg SO4
K2Cr2O7
F. A. S
To know remaining K2 Cr2O7

## Slide 31
Calculations:
Volume of waste water sample taken = 25 mL
Normality of FAS used = N FAS
Volume of F.A.S consumed in back titration = B mL
Volume of F.A.S consumed in blank titration = C mL
So, the volume of K2 Cr2O7 consumed in terms of ‘volume ‘of FAS = (C – B) mL
Therefore, normality of oxygen in waste water N1 = [(C-B )/V] x N FAS
The C.O.D of the sample = N1 x Equiv. wt. of Oxygen in mg.
= N1 x 8 x 1000 = …Y…. mg dm-3
N1 =
Volume of FAS x Normality of FAS
Volume of waste water sample(25mL)

## Slide 32
Argentometric titration (Cl- estimation)[Experiment 5 in Lab course]
https://drive.google.com/file/d/14a333YXP_8NSxKVPCvuGhDjZ9ZBHZrII/view?usp=sharing
Sources Chloride in water : soluble salts MgCl 2 , CaCl 2 , KCl etc
Problems associated with Cl- water : Metallic corrosion of structures , Harmful effects in agriculture..
Principle:
pH =7
Cl- ( in water) + AgNO3 → AgCl (↓) + NO3-
K2CrO4 + 2 AgNO3 (excess) → Ag2CrO4 (↓) + 2 KNO3
(Yellow ) ( brick red)

## Slide 33
Procedure:
Burette : standard AgNO3 solution
Conical Flask : 100 ml the water sample(neutral pH) in to a conical flask ,
Indicator : 2-3 drops of potassium chromate
Colour changes : yellow ( CrO4 2- ion ) to brick red tinge (Ag2CrO4 )
Note the volume of AgNO3 consumed, V1 ml.
Calculations:
Volume of water taken =100 ml,
Volume of AgNO3 = V1 ml
Concentration of AgNO3 = N1
Normality of Chloride in water=
( N 1 X V1/100) = N2
Hence, weight Chloride content in water in mg
= N2 X 35.5 X 1000 = ……..mg dm-3

## Slide 34
Spectro photometric Determination of NO3-
Sources of NO3- in water : synthetic fertilizers , decay of animal and vegetables
Problems associated with excess NO3- Water :
Bitter in taste
causes many physiological disorders like gastrointestinal cancer, Alzheimer,
Reduces oxygen carrying capacity of blood ,
Blue-baby syndrome.

## Slide 35
Determination of Nitrate
Principle:
NO3- reacts with Phenol di sulfonic acid (PDA) to give a nitro derivative in alkaline solution, which is yellow in colour.
The yellow colour intensity is proportional to the concentration of NO3- in sample. a\c to Beer’s law.
A=log 1/T =ɛ Ct
A=absorbance (or)optical density of nitrate ,
T =transmittance ,
C= concentration of nitrate,
t = thickness of cell

## Slide 36
Preparation of a Known conc of NO3- solutions for the Calibration curve:
Take 5, 10, 15, 20 and 25 ml of 0.1N of KNO3 standard solution in 5 separate 50 ml beakers and evaporate to dryness.
Add 2 ml PDA solution and Add 10 ml conc. NH3 to each beaker and dissolve the residue which is quantitatively transferred into a separate 100 ml standard volumetric flasks , dilute up to the mark with distilled water and mix well.
In the same manner , water sample solution is prepared.
Blank solution is prepared by taking 10mL NH3 and 2mL PDA solution in the another 100ml Volumetric flask and dilute it upto the mark with distilled water.
Measure the absorbance or optical density of the prepared solution at 410 nm wave length by colorimeter.
Plot the graph of absorbance Vs concentration of NO3- and find out conc of NO3- in the water sample.

## Slide 37
Calculation
Volume of KNO3 | Concentration of NO3- [VX(62/101)X 6X 10-3 ] | OD/Absorbance
5 |  | 
10 |  | 
15 |  | 
20 |  | 
25 |  | 
30 |  | 
Water sample(a) |  | b
6 g of KNO3 salt dissolves in 1000mL of water as a stock solution
101 g of KNO3 contains = 62 g of nitrate
6 g of KNO3 contains = (62/101)X 6 g of nitrate in 1000mL of KNO3 solution
1mL of KNO3 solution contains = (62/101)X 6 X 10-3 g of nitrate
Result:
‘a’ value on the X-axis corresponds to the concentration of Nitrate in the water sample.

## Slide 38
What is temporary and permanent hardness of water? Explain the determination of total hardness of water by EDTA method.
Discuss the determination of chloride by argentometric method
Define BOD and COD. Why is COD higher than BOD?
What is hard water? What are the causes for hardness of water and why CaCO3 is used to express the hardness of water?
What is potable water? Explain the method of desalination of hard water by reverse osmosis method.
Explain the method of determining nitrate content in water using spectrophotometer.
Explain the gravimetric method of determination of sulfate content in water.
Describe the Winkler’s method of the determination of dissolved oxygen in water
Write note on reverse osmosis