## Slide 1: Input Output Organization

## Slide 2: Accessing I/O devices - A Single bus structure
Bus
I/O de
vice 1
I/O de
vice
n
Processor
Memory

## Slide 3: Accessing I/O devices
Memory mapped IO
IO devices and memory share the same address space.
Move DATAIN,R0
Move R0, DATAOUT
DATAIN and DATAOUT are buffers
I/O devices and the memory may have different address spaces:
Special instructions to transfer data to and from I/O devices.

## Slide 4: Accessing I/O devices
I/O Interface for an input device
I/O
int
erface
decoder
Address
Data and
status registers
Control
circuits
Input device
Bus
Address lines
Data lines
Control lines

## Slide 5: Registers in keyboard and display Interfaces

## Slide 6: Program to read a line from Keyboard and stores in memory buffer and echoes on display( Programmed IO)
Move #LINE , R0
Waitk Test Bit #0, STATUS
Branch=0 Waitk
Move DATAIN, R1
Waitd Test Bit #1,STATUS
Branch=0 Waitd
Move R1, DATAOUT
Move R1,(R0)+
Compare #$0D,R1
Branch!=0 Waitk
Move #$0A, DATAOUT
Call PROCESS

## Slide 7: Program controlled IO
Processor repeatedly checks status flag to achieve synchronization b/w processor and IO device.
  Processor polls the I/O device.
  Two other mechanisms used for synchronizing data transfers between the processor and memory:
  Interrupts
  DMA

## Slide 8: INTERRUPTS
Drawback of programmed IO
processor time is wasted in waiting for IO device without doing useful processing.
Waiting period can be avoided by allowing IO devices to notify the processor when they are ready
Done through Hardware Interrupts
Interrupt Service Routine(PRINT function)
Interrupt latency (Time b/w receipt of interrupt req and start of execution of interrupt service routine.)
here
Interrupt
occurs
M
i
2
1
i
1
+
Transfer of control through interrupts
Program 1 Program 2
COMPUTE routine PRINT routine
Interrupts save PC and status register
Some interrupts save the registers some not

## Slide 9: Interrupts (contd..)
Treatment of an interrupt-service routine is very similar to that of a subroutine.
However there are significant differences:
  A subroutine performs a task that is required by the calling program.
  Interrupt-service routine may not have anything in common with the program it interrupts.
  Interrupt-service routine and the program that it interrupts may belong to different users.
  As a result, before branching to the interrupt-service routine, not only the PC, but other information such as condition code flags, and processor registers used by both the interrupted program and the interrupt service routine must be stored.
  This will enable the interrupted program to resume execution upon return from interrupt service routine.

## Slide 10: Interrupts (contd..)
Saving and restoring information can be done automatically by the processor or explicitly by program instructions.
Saving and restoring registers involves memory transfers:
  Increases the total execution time.
  Increases the delay between the time an interrupt request is received, and the start of execution of the interrupt-service routine. This delay is called interrupt latency.
In order to reduce the interrupt latency, most processors save only the minimal amount of information:
  This minimal amount of information includes Program Counter and processor status registers.
Any additional information that must be saved, must be saved explicitly by the program instructions at the beginning of the interrupt service routine.

## Slide 11: Interrupt Hardware
Single interrupt line is used to serve n devices
Closing of switches makes voltage to drop to 0 and INTR received by processor will goto 1
If all switches are open voltage will be vdd
INTR=INTR1+INTR2+INTR3+………+INTRn

## Slide 12: Interrupts (contd..)
When a processor receives an interrupt-request, it must branch to the interrupt service routine.
It must also inform the device that it has recognized the interrupt request.
This can be accomplished in two ways:
  Some processors have an explicit interrupt-acknowledge control signal for this purpose.
  In other cases, the data transfer that takes place between the device and the processor can be used to inform the device.

## Slide 13: Interrupts (contd..)
Interrupt-requests interrupt the execution of a program, and may alter the intended sequence of events:
  Sometimes such alterations may be undesirable, and must not be allowed.
  For example, the processor may not want to be interrupted by the same device while executing its interrupt-service routine.
Processors generally provide the ability to enable and disable such interruptions as desired.
One simple way is to provide machine instructions such as Interrupt-enable and Interrupt-disable for this purpose.
To avoid interruption by the same device during the execution of an interrupt service routine:
  First instruction of an interrupt service routine can be Interrupt-disable.
  Last instruction of an interrupt service routine can be Interrupt-enable.

## Slide 14: How to avoid successive interruptions
Enable and Disable instruction in beginning and ending of ISR
Using PS register enable bit
Edge triggered :
Interrupt request line of processor will respond to interrupt handling circuit for leading edge of the signal.
Processor will receive only one request regardless of how long the line is activated.

## Slide 15: Enabling and Disabling Interrupts- Sequence of actions
The device raises an interrupt request
The processor interrupts the program currently being executed
Interrupts are disabled by changing the control bits in PS.
The device is informed that its request has been recognized and in response , it deactivates the interrupt request signal
The action requested by the interrupt service routine
Interrupts are enabled and execution of the interrupted program is resumed.

## Slide 16: Handling Multiple Interrupts
Multiple I/O devices may be connected –HOW TO ADDRESS
How does the processor know which device has generated an interrupt?
How does the processor know which interrupt service routine needs to be executed?
When the processor is executing an interrupt service routine for one device, can other device interrupt the processor?
If two interrupt-requests are received simultaneously, then how to break the tie?

## Slide 17: How to recognize the interrupted device
ISR Polls the devices connected.
If the IRQ bit=1 then serves the device
Polling mechanism is easy, but time consuming to query the status bits of all the I/O devices connected to the bus.

## Slide 18: Vectored Interrupts
Device identifies itself to the processor by sending a code.
CODE is starting addr(interrupt vector) of ISR(4 to 8 bits code length) but need not be ISR
IVPC
INTR(Device activates when it is ready with interrupt)
INTA(Processor activates when it is ready to receive INT)

## Slide 19: Interrupt Nesting- Priority
I/O devices are organized in a priority structure:
  An interrupt request from a high-priority device is accepted while the processor is executing the interrupt service routine of a low priority device.
A priority level is assigned to a processor that can be changed under program control.
  Priority level of a processor is the priority of the program that is currently being executed.
  When the processor starts executing the interrupt service routine of a device, its priority is raised to that of the device.
  If the device sending an interrupt request has a higher priority than the processor, the processor accepts the interrupt request.
Notes: Repeat that multiple I/O devices may be connected to the processor. These multiple I/O devices may be organized according a certain priority. When the processor is servicing an interrupt from a device, only devices which have higher priority can interrupt the processor. That is, only devices which have higher priority can interrupt the processing of the ISR of the device of lower priority.
In order to implement this scheme, a priority level is assigned to a processor. This priority level can be changed under program control or it depends on which program is currently being executed by the processor. That is, the priority of the processor is the priority of the program that the processor is currently executing. When the processor receives an interrupt request from a device, and starts executing the ISR of that device, its priority is raised to that of the device. Now, if another device wants to interrupt the processor, then it is allowed to do so, only if its priority is higher than the priority of the processor which is set to the priority of the ISR of the device.

## Slide 20: Multiple Priority Levels
Priority arbitration
Device 1
Device 2
Device
p
Processor
INTA1
I
N
T
R
1
I
N
T
R
p
INTA
p
Each device has a separate interrupt-request and interrupt-acknowledge line.
Each interrupt-request line is assigned a different priority level.
Interrupt requests received over these lines are sent to a priority arbitration circuit
in the processor.
If the interrupt request has a higher priority level than the priority of the processor,
then the request is accepted.

## Slide 21: Simultaneous Requests-No separate INTR line
Which interrupt request does the processor accept if it receives interrupt requests from two or more devices simultaneously?.
If the I/O devices are organized in a priority structure, the processor accepts the interrupt request from a device with higher priority.
  Each device has its own interrupt request and interrupt acknowledge line.
  A different priority level is assigned to the interrupt request line of each device.
However, if the devices share an interrupt request line, then how does the processor decide which interrupt request to accept?

## Slide 22: Daisy chain
Polling
Vectored Interrupt
Daisy chain
Processor
Device 2
I
N
T
R
INTA
Device
n
Device 1

## Slide 23: Arrangement of Priority Groups
Device
Device
circuit
Priority arbitration
Processor
Device
Device
I
N
T
R
1
I
N
T
R
p
INTA1
INTA
p

## Slide 24: Controlling Device Requests
Devices used in a program are allowed to generate interrupt requests.
To control which devices are allowed to generate interrupt requests, the interface circuit of each I/O device has an interrupt-enable bit.
  If the interrupt-enable bit in the device interface is set to 1, then the device is allowed to generate an interrupt-request.
Interrupt-enable bit in the device’s interface circuit determines whether the device is allowed to generate an interrupt request.
If DEN(Device)=1DIRQ(Processor) , KEN=1KIRQ

## Slide 25: Using interrupts to read line of characters

## Slide 26: Exceptions
  Error in the data stored.
  Error during the execution of an instruction.
Types of exceptions are:
  Recovery from errors
  Debugging
  Privilege exception
Recovery from exception Exception service routine
Divide by zero, un recognized OP code

## Slide 27: Debugger
Debugger uses exceptions to provide important features:
  Trace—Exception occurs after executing every instruction
  Breakpoints—Interrupted at specific point
Trace mode:
  Exception occurs after the execution of every instruction.
  Debugging program is used as the exception-service routine.
Breakpoints:
  Exception occurs only at specific points selected by the user.
  Debugging program is used as the exception-service routine.

## Slide 28: Privilege exception
Certain instructions can be executed only when the processor is in the supervisor mode. These are called privileged instructions.
If an attempt is made to execute a privileged instruction in the user mode, a privilege exception occurs.
Privilege exception causes
  Processor to switch to the supervisor mode,
  Execution of an appropriate exception-servicing routine.
Notes: Recall privilege mode and supervisor mode. Certain instructions can only be executed in the supervisor mode. If an attempt is made to execute the instruction in the user mode, then an privilege exception occurs. Privilege exception causes the processor to switch to the supervisor mode, and execution of an appropriate service routine.

## Slide 29: DIRECT MEMORY ACCESS
Drawbacks of previous approaches
Restoring PC and other state information
Processor has to poll IO device/ waits for device to send INT
Transfers large block of data at high speed
  control unit may be provided to transfer a block of data directly between an I/O device and the main memory, without continuous intervention by the processor.

## Slide 30: DIRECT MEMORY ACCESS
Control unit which performs these transfers is part of the I/O device’s interface circuit. This control unit is called as a DMA controller (performs functions of processor).
The requested program will be put in the blocked state.
The operation of the DMA controller must be under the control of a program executed by the processor. That is, the processor must initiate the DMA transfer.
Once the DMA controller completes the DMA transfer, it informs the processor by raising an interrupt signal.

## Slide 31: Direct Memory Access (contd..)
Direct Memory Access (DMA):
  A special control unit may be provided to transfer a block of data directly between an I/O device and the main memory, without continuous intervention by the processor.
Control unit which performs these transfers is a part of the I/O device’s interface circuit. This control unit is called as a DMA controller.
DMA controller performs functions that would be normally carried out by the processor:
  For each word, it provides the memory address and all the control signals.
  To transfer a block of data, it increments the memory addresses and keeps track of the number of transfers.
Notes: This alternative approach is called as direct memory access. DMA consists of a special control unit which is provided to transfer a block of data directly between an I/O device and the main memory without continuous intervention by the processor.
A control unit which performs these transfers without the intervention of the processor is a part of the I/O device’s interface circuit, and this controller is called as the DMA controller.
DMA controller performs functions that would be normally be performed by the processor. The processor will have to provide a memory address and all the control signals. So, the DMA controller will also provide with the memory address where the data is going to be stored along with the necessary control signals. When a block of data needs to be transferred, the DMA controller will also have to increment the memory addresses and keep track of the number of words that have been transferred.

## Slide 32: DMA
To initiate the DMA transfer, the processor informs the DMA controller of:
  Starting address,
  Number of words in the block.
  Direction of transfer (I/O device to the memory, or memory to the I/O device).
R/W =1 Read(MIO)
Done=1 when completed Transfer
IE=1 when ready for next transfer
IRQ=1 when interrupt is requested

## Slide 33: Direct Memory Access
memory
Processor
System bus
Main
Keyboard
Disk/DMA
controller
Printer
DMA
controller
Disk
Disk
DMA controller connects a high-speed network to the computer bus.
Disk controller, which controls two disks also has DMA capability. It provides two DMA channels.
It can perform two independent DMA operations, as if each disk has its own DMA controller.
The registers to store the memory address, word count and status and
control information are duplicated.
Network
Interface
Notes: Let us consider a memory organization with two DMA controllers. In this memory organization, a DMA controller is used to connect a high speed network to the computer bus. In addition, disk controller which also controls two disks may have DMA capability. The disk controller controls two disks and it also has DMA capability. The disk controller provides two DMA channels. The disk controller can two independent DMA operations, as if each disk has its own DMA controller. Each DMA controller has three registers, one to store the memory address, one to store the word count, and the last to store the status and control information. There are two copies of these three registers in order to perform independent DMA operations. That is, these registers are duplicated.

## Slide 34: Direct Memory Access
Processor and DMA controllers have to use the bus in an interwoven fashion to access the memory.
  DMA devices are given higher priority than the processor to access the bus.
  Among different DMA devices, high priority is given to high-speed peripherals such as a disk or a graphics display device.
Processor originates most memory access cycles on the bus.
  DMA controller can be said to “steal” memory access cycles from the bus. This interweaving technique is called as “cycle stealing”.
An alternate approach is the provide a DMA controller an exclusive capability to initiate transfers on the bus, and hence exclusive access to the main memory. This is known as the block or burst mode.
Notes: Processor also has to transfer data to and from the main memory. Also, the DMA controller is responsible for transferring data to and from the I/O device to the main memory. Both the processor and the DMA controller have to use the external bus to talk to the main memory. Usually, DMA controllers are given higher priority than the processor to access the bus. Now, we also need to decide the priority among different DMA devices that may need to use the bus. Among these different DMA devices, high priority is given to high speed peripherals such as a disk or a graphics display device.
Usually, the processor originates most cycles on the bus. The DMA controller can be said to steal memory access cycles on from the bus. Thus, the processor and the DMA controller use the bus in an interwoven fashion. This interweaving technique is called as cycle stealing.
An alternate approach would be to provide DMA controllers exclusive capability to initiate transfers on the bus, and hence exclusive access to the main memory. This is known as the block mode or the burst mode of operation.