## Slide 1: Machine Instructions and Programs

## Slide 2
Machine Instructions and Programs
Memory Locations and Ad dress, Byte addressability, Big-endian and Little-endian assignments, Word Alignment, Accessing Numbers, Characters and Character strings, memory Operation, Instruction and Instruction Sequencing, Register Transfer Notation, Assembly Language Notation.

## Slide 3: Objectives
Machine instructions and program execution, including branching and subroutine call and return operations.
Addressing methods for accessing register and memory operands.
Assembly language for representing machine instructions, data, and programs.
Program-controlled Input/Output operations.

## Slide 4: Memory Locations, Addresses, and Operations

## Slide 5: Memory Location, Addresses, and Operation
Memory consists of many millions of storage cells, each of which can store 1 bit.
Data is usually accessed in n-bit groups. n is called word length.
second word
first word
Figure Memory words.
last word
i
th word
•
•
•
•
•
•
N bits

## Slide 6: Memory Location, Addresses, and Operation
32-bit word length example
(b) Four characters
character
character
character
character
(a) A signed integer
Sign bit:
for positive numbers
for negative numbers
ASCII
ASCII
ASCII
ASCII
32 bits
8 bits
8 bits
8 bits
8 bits
b
31
b
30
b
1
b
0
b
31
0
=
b
31
1
=
•
•
•

## Slide 7: Memory Location, Addresses, and Operation
To retrieve information from memory, either for one word or one byte (8-bit), addresses for each location are needed.
A k-bit address memory has 2k memory locations, namely 0 – 2k-1, called memory space.
24-bit memory: 224 = 16,777,216 = 16M (1M=220)
32-bit memory: 232 = 4G (1G=230)
1K(kilo)=210
1T(tera)=240

## Slide 8: Memory Location, Addresses, and Operation
It is impractical to assign distinct addresses to individual bit locations in the memory.
The most practical assignment is to have successive addresses refer to successive byte locations in the memory – byte-addressable memory.
Byte locations have addresses 0, 1, 2, … If word length is 32 bits, they successive words are located at addresses 0, 4, 8,…

## Slide 9: Big-Endian and Little-Endian Assignments
Big-Endian: lower byte addresses are used for the most significant bytes of the word
Little-Endian: opposite ordering. lower byte addresses are used for the less significant bytes of the word

## Slide 10
2
k
4
-
2
k
4
-
0
0
4
4
2
k
1
-
2
k
2
-
2
k
3
-
2
k
4
-
3
2
1
0
7
6
5
4
•
•
•
2
k
4
-
2
k
3
-
2
k
2
-
2
k
1
-
0
1
2
3
4
5
6
7
•
•
•
Address Byte Address Address Byte Addess
(a) Big-endian assignment
(b) Little-endian assignment
Figure Byte and word addressing.

## Slide 11: Memory Location, Addresses, and Operation
Address ordering of bytes
Word alignment
  Words are said to be aligned in memory if they begin at a byte addr. that is a multiple of the num of bytes in a word.
    16-bit word: word addresses: 0, 2, 4,….
    32-bit word: word addresses: 0, 4, 8,….
    64-bit word: word addresses: 0, 8,16,….
Access numbers, characters, and character strings

## Slide 12: Memory Operation
Load (or Read or Fetch)
Copy the content. The memory content doesn’t change.
Address – Load
Registers can be used
Store (or Write)
Overwrite the content in memory
Address and Data – Store
Registers can be used

## Slide 13: Instruction and Instruction Sequencing

## Slide 14: “Must-Perform” Operations
Data transfers between the memory and the processor registers
Arithmetic and logic operations on data
Program sequencing and control
I/O transfers

## Slide 15: CPU Organization
Single Accumulator
  Result usually goes to the Accumulator
  Accumulator has to be saved to memory quite often
General Register
  Registers hold operands thus reduce memory traffic
  Register bookkeeping
Stack
  Operands and result are always in the stack

## Slide 16: Register Transfer Notation
Identify a location by a symbolic name standing for its hardware binary address (LOC, R0,…)
Contents of a location are denoted by placing square brackets around the name of the location (R1←[LOC], R3 ←[R1]+[R2])
Register Transfer Notation (RTN)

## Slide 17: Assembly Language Notation
We consider different types of machine
Three address machine
Two address machine
One address machine
Zero address machine

## Slide 18
Three address Instructions:
ADD R1, R2, R3; R3  [R1] + [R2]
SUB R1, R2, R3; R3 [R1] – [R2]
MUL R1, R2, R3; R3 [R1] * [R2]
DIV R1, R2, R3; R3 [R1] / [R2]
LOAD M, R ; R  [ M ]
STORE R, M ; [M]  [R]

## Slide 19
Example: Evaluate the following expression x=(A+B)  (C+D) by three-Address
  ADD A, B, R1 ; R1 ← M[A] + M[B]
  ADD C, D, R2 ; R2 ← M[C] + M[D]
  MUL R1, R2, X ; M[X] ← R1  R2

## Slide 20
Two address Instruction Format:
ADD R1, R2; R2 [R2] +[R1]
SUB R1, R2; R2 [R2] – [R1]
MUL R1, R2; R2  [R2] * [R1]
DIV R1, R2; R2 [R2] / [R1]
LOAD M, R ; R [ M ]
STORE R, M ; [M]  R

## Slide 21
One address Instruction format:
In One address instruction machine, one register is assumed to be accumulator. Accumulator is shown as Acc. in the instruction.
ADD A; [Acc]  [Acc] + M[A]
SUB A; [Acc] [Acc] - M[A]
MUL A [Acc] [Acc] * M[A]
DIV A [Acc ][Acc ]/ M[A]
LOAD A [Acc] M[A]
STORE A M[A] [ Acc]

## Slide 22
Example: Evaluate (A+B)  (C+D)
One-Address
  LOAD A ; ACc ← M[A]
  ADD B ; ACc← ACc + M[B]
  STORE T ; M[T] ← ACc
  LOAD C ; ACc ← M[C]
  ADD D ; ACc ← ACc + M[D]
  MUL T ; ACc ← ACc  M[T]
  STORE X ; M[X] ← ACc

## Slide 23
Zero Address Instructions machine
It is also called stack machine. In this machine, the operation takes place on the top of the stack. The procedure is that the arithmetic operation that takes place on the top of the stack and one location below it.
ADD ; TOS[STACK] = TOS[STACK] + TOS-1[STACK-1]
SUB ; TOS[STACK] = TOS[STACK] - TOS-1[STACK-1]
MUL ; TOS[STACK] = TOS[STACK] * TOS-1[STACK-1]
DIV ; TOS[STACK] = TOS[STACK] / TOS-1[STACK-1]
PUSH A; TOS[STACK] = A
POP A ; A = TOS[STACK]

## Slide 24: Instruction Formats
Example: Evaluate (A+B)  (C+D)
Zero-Address
  PUSH A ; TOS ← A
  PUSH B ; TOS ← B
  ADD ; TOS ← (A + B)
  PUSH C ; TOS ← C
  PUSH D ; TOS ← D
  ADD ; TOS ← (C + D)
  MUL ; TOS ← (C+D)(A+B)
  POP X ; M[X] ← TOS

## Slide 25: Using Registers
Registers are faster
Shorter instructions
  The number of registers is smaller (e.g. 32 registers need 5 bits)
Potential speedup
Minimize the frequency with which data is moved back and forth between the memory and processor registers.

## Slide 26: UNIT II
Chapter 2

## Slide 27: Instruction Execution and Straight-Line Sequencing
Begin execution here
Address Contents
Move R0, C
Move A, R0
Add B, R0
i
+ 8
i
C
B
A
i
+ 4
Figure A program for C ¬ [A] + [B].
Three – Instruction program segment
Data for the program

## Slide 28
Program Counter: Contains the address of instruction to be executed next.
Assumptions:
  - One memory operand per instruction
  - 32-bit word length
  - Memory is byte addressable
  Full memory address can be directly specified in a single-word instruction
Two-phase procedure
Instruction fetch IR
Instruction execute

## Slide 29: Branching
i | Move NUM1 , R0
i+4 | ADD NUM2, R0
i+8 | ADD NUM3, R0
 | .
 | .
 | .
i+4n-4 | ADD NUMn, R0
i+4n | Move R0, SUM
 | .
 | .
 | .
Sum | 
NUM1 | 
NUM2 | 
NUMn | 
Program to add ‘n’ nums which is stored from the location NUM1 to NUMn. Store the sum in the memory location SUM.
This program does a routine operation of adding from the consecutive locations. Can this be optimized?

## Slide 30: Branching
n
Using a loop to add n numbers.
loop
Program
MOVE N, R1
CLEAR R0
Determine the address of “Next number and add it to R0
Decrement R1
Branch > 0 LOOP
Move R0, SUM
NUM n
NUM2
NUM1
N
SUM
.
.
.

## Slide 31: Condition Codes
Condition code flags
Condition code register / status register
N (negative)
Z (zero)
V (overflow)
C (carry)
Different instructions affect different flags

## Slide 32: Conditional Branch Instructions
Example:
  A: 1 1 1 1 0 0 0 0
  B: 0 0 0 1 0 1 0 0
A: 1 1 1 1 0 0 0 0
+(−B): 1 1 1 0 1 1 0 0
1 1 0 1 1 1 0 0
C = 1
S = 1
V = 0
Z = 0

## Slide 33: Status Bits
ALU
V
Z
S
C
Zero Check
Cn
Cn-1
Fn-1
A
B
F

## Slide 34: Addressing Modes

## Slide 35: Generating Memory Addresses
Addressing mode is a means of finding the different ways in which the location of an operand is specified in the instruction.
How to specify the address of branch target?
Can we give the memory operand address directly in a single Add instruction in the loop?
Use a register to hold the address of NUM1; then increment by 4 on each pass through the loop.

## Slide 36
The different types of addressing modes are –
Register addressing mode
Register Indirect addressing mode
Absolute/Direct addressing mode
Immediate addressing mode
Indirect addressing mode
Indexed addressing mode
Base with index and offset
Relative addressing mode
Autoincrement mode
Autodecrement mode

## Slide 37
Register Addressing mode:
In this addressing mode, the operand is the contents of a processor register. The name of the register is in the instruction.
Example: MOVE R1, R2

## Slide 38
Absolute/ Direct Addressing mode:
In Absolute addressing mode, the address of the operand is given in the instruction itself.
Example: MOVE LOC, R0
Immediate Addressing mode:
In this addressing mode, the data itself is immediately given in the instruction itself.
Example: MOV 200immediate, R0
MOV #200, R0

## Slide 39
Indirect addressing mode:
There are two Indirect addressing mode.
(a) Register Indirect addressing mode:
The effective address of the memory operand is the contents of a register which is mentioned in the instruction. It means the memory is accessed by using the address available in the register.
Example: MOVE [R2], R0
ADD (R1),R0
Here the register R2 contains the memory address. The data is moved from the memory location pointed by register R2 and moved to register R2

## Slide 40
(b) Memory Indirect Addressing Mode:
In this addressing mode, the address of the operand is available in the memory.
AR = 101
100
101
102
103
104
Memory
0 1 0 4
1 1 0 A
MOV [AR], R0
Drawback:
Mem is accessed twice to get an operand so not well suited
110A
R0

## Slide 41
Implied Addressing mode
In this addressing mode, it is understood that the operand is on the register.
Example: ADD
In zero addressing mode the Top of the Stack is understood.

## Slide 42
Autoincrement Addressing Mode:
In this mode the effective address of the operand id the contents of a register specified in the instruction. After accessing the operand, the contents of this register are automatically incremented to point to the next item in a list.
(Ri)+
Example: Add (R2)+, R0
Contents of memory pointed by R2 is added to contents of R0 and the result is stored in register R0. After the addition operation the register R2 is increment by the operand size.
Note: If the operand is byte data then the increment is one.
If the operand is 16bits then the increment is 2
If the operand is 32 bits then the increment is 4.

## Slide 43
Auto decrement Addressing Mode:
In this mode the effective address mode, the content of a register specified in the instruction are first automatically decremented and are then used as the effective address of the operand.
- (Ri)
The actions performed by the Autoincrement and Autodecrement addressing mode can be achieved by using two instructions. One to access the operand and the other to increment or decrement the register that contains the operand.

## Slide 44
Indexed Addressing Mode:
In this addressing mode the effective address of the operand is generated by adding a constant value to the contents of a register.
  EA = X+[Ri]
100
101
102
103
104
Memory
R2 = 100
1 1 0 A
X1 = 2
+
X (Ri)
Where X denotes the constant value contained in the instruction and Ri is the name of the register involved.
Example:Add X1(R2),R0
If X1 =2, and R2=100 then the figure shows that the contents of memory 102 is accessed to add with R0 and stored in R0

## Slide 45
100
101
102
103
104
Memory
0
1
2
Relative Addressing Mode
In this addressing mode, the address of the operand is calculated relative to the PC.
AR = 100
1 1 0 A
PC = 2
+
Program
Data
Could be Positive or Negative (2’s Complement)
Example:
Branch > 0 LOOP
The effective address of the operand is calculated with respect to PC
  EA = PC + Relative Addr

## Slide 46
Base Register addressing mode
  EA = Base Register + Relative Addr
  BR = Base Register; AR = Relative Address
100
101
102
103
104
Memory
BR = 100
0 0 0 A
AR = 2
+
Could be Positive or Negative (2’s Complement)
Usually points to the beginning of an array
0 0 0 5
0 0 1 2
0 1 0 7
0 0 5 9
In this addressing mode the base register contents is considered to be a part of the
address. This value is added to the Relative address to calculate the effective address.

## Slide 47
The different ways in which the location of an operand is specified in an instruction are referred to as addressing modes.
Name
Assembler
syntax
Addressing
function
Immediate
#V
alue
Op
erand
=
V
alue
Register
R
i
EA
=
R
i
Absolute
(Direct)
LOC
EA
=
LOC
Indirect
(R
i
)
EA
=
[R
i
]
(LOC)
EA
=
[LOC]
Index
X(R
i
)
EA
=
[R
i
]
+
X
Base
with
index
(R
i
,R
j
)
EA
=
[R
i
]
+
[R
j
]
Base
with
index
X(R
i
,R
j
)
EA
=
[R
i
]
+
[R
j
]
+
X
and
offset
Relative
X(PC)
EA
=
[PC]
+
X
Autoincremen
t
(R
i
)+
EA
=
[R
i
]
;
Incremen
t
R
i
Autodecrement
(R
i
)
Decremen
t
R
i
;
EA
=
[R
i
]


## Slide 48
Immediate data can be either in binary, decimal or Hexadecimal. To identify each of the number system a symbol is prefix is used. It is shown in the table.
Number | Number System | Prefix symbol | Example
32 | Decimal |  | Add #5, R6
10101110 | Binary | % | MOV #%10101110
5D | Hexa decimal | $ | MOV $#5D, R5

## Slide 49: Assembly Language

## Slide 50
Programs written using 0’s and 1’s are machine instructions.
Machine instructions are difficult to write or to read. Hence mnemonic are used to represent the operations such as
ADD
SUM
MOVE
Similarly, R3 is the notation used to refer to register 3.
A complete set of such symbolic names and rules for their use constitute a programming language, generally referred to as assembly language.
The set of rules for using the mnemonics is the specification of complete instruction and program is called the syntax of the language

## Slide 51
Assembler system program is stored in memory.
User written assembly level program is entered in primary memory.
When assembled, the assembly level user program is converted to machine level program and stored in sequential memory location.
Assembler has a standard with mnemonic followed by operand or operands. There are delimiters between mnemonic, register R1 and memory ‘SUM’ in the example shown below.
Example: Move R1, SUM
Assembler
Source Program
Object Program

## Slide 52
Assembler needs some information to understand and interpret what user wants. These extra information that is provided to make Assembler understand is called assembler directive.
Assembler directives:
Assembler directives are the instructions to the assembler that specifies information needed to translate the source program into the object program. Assembler directives are not translated to object code by the assembler. Some of them are discussed below.
EQUATE: SUM EQU 100
It informs the assembler that SUM should be replaced by the value 200, wherever it appears in the program

## Slide 53
Origin: It tells the assembler program where in the memory to place the block that follows.
Example: ORIGIN 198
DATAWORD 64
The data that is following the ORIGIN, 198 is the location from where the next data is being stored.
DATAWORD: It is an assembler directive stating that the data that is following it is 16 bits data. In the above example, the memory location following ORIGIN location 198 a memory of 16 bits are used to store the data.
It is possible to use a variable name before the DATAWORD indicating that the variable name mentioned is 16 bits.
Address | Data/Opcode
199 | 64

## Slide 54
END: The end directive is used to tell the assembler that the program has ended. There are no more instructions following this statement for assembly.
Usually, following the END statement a variable is used which is the label of the start of the program. The label points to the address of the location at which execution of the program is to begin.
Assembly Language Format:
Assembly language program is usually written in a specific format to enable the assembler to tokenise each token for assembling the program. However it is also convenient for the user the read the assembly program.
There are four fields separated by appropriate delimiters.
LABEL OPERATION OPERANDS COMMENTS

## Slide 55
Typically, one or more blank characters are used to separate the fields.
Label: It is an optional field. A name is associated with the memory address is mentioned in this field.
Operation Field: This field contains Operation code mnemonic of the desired instruction.
Operand Field: It is an optional field. If the Operation code requires one of more operand it is mentioned in this field.
Comments: It is optional field. It is used for documentation of the program. The assembler will ignore this field.

## Slide 57: Stacks and Queues
Control and info linkage b/w main program and subroutine is through stacks
LIFO/FILO data structure

## Slide 58: Stack operations
PUSH
Subtract #4,SP
Move NEWITEM,(SP)
POP
MOVE (SP),ITEM
ADD #4,SP

## Slide 59: Effect of PUSH and POP operation

## Slide 60: Use of Auto decrement and Increment for PUSH and POP operation
PUSH
MOVE NEWITEM, -(SP)
POP
MOVE (SP)+, ITEM

## Slide 61: SAFE POP operation
Compare #2000,SP
Branch>0 EMPTYERROR
Move (SP)+,ITEM

## Slide 62: SAFE PUSH operation
Compare #1500,SP
Branch<=0 FULLERROR
Move NEWITEM,-(SP)

## Slide 63: Queues
FIFO
Difference b/w Stack and Queue
stack uses single pointer and queue two

## Slide 64: SUBROUTINES
Saves space
Subroutine call
Subroutine return
Subroutine linkage method(using linkage register)

## Slide 65: SUBROUTINES
Call instruction is a special branch instruction that performs following operations
Store the contents of the PC in the linkage register
Branch to target address specified by the instn
Return instruction is a special branch instrn that performs following operations
Branch to the address contained in the link register

## Slide 66: SUBROUTINES

## Slide 67: Subroutine nesting and Processor stack
Subroutine call another subroutine
Single link register is not sufficient
Stored on processor stack

## Slide 68
END

## Slide 70
Instruction Set
The instruction set of a computer is machine dependent. It is required to know the instruction set to write a program. Instruction set can be grouped based on the type of the operation. The different group are –
Data Transfer group
Arithmetic and logic group
Branch transfer group
Machine group
Data Transfer Group:
Data transfer group of instructions consists of all the data transfer from register to register, register to memory, memory to registry and input output instructions. There is no instruction to move data from memory to memory transfer.

## Slide 71
Move R1, R2 ; Register addressing mode
Move #5, R3 ; Immediate addressing mode
Move (R1), R2 ; Register indirect addressing mode
Move –(R5), R0; Auto decrement addressing mode
Move X(R2), R1; Index addressing mode
Movemultiple (R0-R3), -SP ; This is an instruction where multiple registers are moved on the top of the stack. Before the contents of register is saved on the top of the stack, the contents of the stack pointer is decremented by two. The process continues till all the register is saved on the top of the stack.
Movemultiple(SP)+, (R0-R3) : The data from the top of the stack is moved to the registers mentioned in the instruction.

## Slide 72
Input Data Transfer Instruction:
Data from input devices can be accessed using MoveByte instruction. Before moving the data from the input device, which is much slower than the CPU, the program checks whether the device has made the data available by seeing a flag SIN. If the SIN flag is 0, the data is not ready and if the SIN flag is 1, then the data is available in I/O area DATAIN and the data can be readt
READWAIT BRANCH to READWAIT if SIN=0
MOVEByte DATAIN, R1
Output Data Transfer Instruction:
Data can be sent out of the processor much faster than the device can accept. To make sure that data is not lost, it is

## Slide 73
R 0equired to check whether the device is ready to receive data. This is being done by looking into a flag called Sout. If Sout = 0 then the device is not ready. If Sout =1, then device is ready to receive the data. It is required to write an instruction to make the program check Sout flag and wait there till the device is ready to accept. Once the device is ready send the data to DATAOUT register.
WriteWait Branch WriteWait if Sout = 0
Movebyte R1, DATAOUT
MOVE (R1, R2), R3 ; This is an instruction which is multi-dimensional addressing mode. The contents of R1 and R2 are added to access the data from memory and store the result in register R3. R1 is for one of the index and R2 is for the second index in two dimensional data access.

## Slide 74
Arithmetic and Logical group:
Arithmetic instructions consists of Addition, Subtraction, Multiplication and division instructions.
Addition:
ADD R1, R2; Register addressing mode
ADD #6, R3; Immediate addressing mode
ADD (R4), R2 ; Register indirect addressing mode
ADD X(R5), R4; Index addressing mode
ADD (R1, R3), R8; Multi index addressing mode
INCREMENT R5; R5 = R5 + 1

## Slide 75
Subtraction:
SUB R1, R2; Register addressing mode
SUB #6, R3; Immediate addressing mode
SUB (R4), R2 ; Register indirect addressing mode
SUB X(R5), R4; Index addressing mode
SUB (R1, R3), R8; Multi index addressing mode
Decrement R1; R1=R1-1

## Slide 76
Multiplication:
MUL R1, R2; Register addressing mode
MUL #6, R3; Immediate addressing mode
MUL (R4), R2 ; Register indirect addressing mode
MUL X(R5), R4; Index addressing mode
MUL (R1, R3), R8; Multi index addressing mode

## Slide 77
Division:
DIV R1, R2; Register addressing mode
DIV #6, R3; Immediate addressing mode
DIV (R4), R2 ; Register indirect addressing mode
DIV X(R5), R4; Index addressing mode
DIV (R1, R3), R8; Multi index addressing mode

## Slide 78
Logical and Bit manipulation instructions:
NOT dest ; 1’s Complement
NEGATE dest ; 2’s complement
AND dest, source ; dest = dest AND source
OR dest, source ; dest = dest OR source
COMPARE dest, source ; Source – dest takes place and the result is not stored in memory by the flags are affected.
LshiftL count, dest ; Logical shift left.
Register
C

## Slide 79
LshiftR count, dest ; Logical shift Right. LShiftR #2, R0
AShiftR count, dest; Arithmetic Shift Right. AShiftR #3, R4
RotateL Count, dest ; Rotate destination without carry
Rotate #2, R0
RotateLC count, dest; Rotate destination through carry
RotateLC #3, R1
Register
C
Register
C
Register
C
Register
C

## Slide 80
RotateR count, dest; Rotate right without carry ; RotateR #2, R2
RotateRC count, dest; Rotate right with carry; RorateRC #4, R5
Register
C
Register
C